## Slide 1: Type Qualifier in ‘C’
const & volatile

## Slide 2: volatile

## Slide 3: volatile
Tell compiler not to invoke any optimization on the variable operation.
Enforce the compiler not to do any optimization on the variables operation(read/write), which are declared as volatile.
A variable must be declared using a variable qualifer when where is a possibility of unexpected changes in the variable value.

## Slide 4: When to use ‘volatile’ qualifier?
Use volatile when your code is dealing with beblow scenarios
Memory-mapped peropheral register of the MCU.
Multiple tasks accessing global variables(read/write) in an RTOS multithreaded application.
When a global variable is used to share data beween the main code and ISR code.

## Slide 5: Case 1: volatile data
  uint8_t volatile my_data;
  Read like this
  my_data is a volatile variable of type unsigned integer_8

## Slide 6: Case 2: non-volatile pointer to volatile data
uint8_t volatile * pStatusReg;
  Read like this
  pStatusReg is non-volatile pointer, pointing to volatile data of type unsigned integer_8
  Use case:
  This is a perfect case of accessing memory-mapped register.

## Slide 7: Case 3: volatile pointer to non-volatile data
uint8_t * volatile pStatusReg;
Read like this
pStatusReg is a volatile pointer, pointing to non–volatile data of type unsigned integer_8

## Slide 8: Case 4: volatile pointer to volatile data
uint8_t volatile *volatile pStatusReg;
Read like this
pStatusReg is a volatile pointer, pointing to volatile data of type unsigned integer_8
很少用！

## Slide 9: const

## Slide 10: const
Case 1:
  uint8_t const data = 50;
  Like pi = 3.14
  data內容不能修改

## Slide 11
Case 2: Modifiable pointer and constant data
  uint8_t const *pData = (uint8_t *)0x40000000;
  Data is read-only
  pData is a pointer pointing to read-only data.
  Allowed Not allowed
  pData = (uint8_t *)0x5000000; *pData = 50;
  pData = (uint8_t *)0x6000000;
  pData = (uint8_t *)0x7000000;
  pData 可以為該pointer分配不同的位址

## Slide 12
void copy_src_to_dst(uint_8 const *src, uint8_t *dst, …)
{
for(uint32_t i = 0; i < len; i ++)
{
*dst = *src;
dst++;
src++;
}
}

## Slide 13
Case 3: Modifiable data and constant pointer
uint8_t * const pData = (uint8_t *)0x40000000;
pData is fixed => 無法為pointer分配新的位址
Allowed Not allowed
*pData =50; pData = (uint8_t *)0x50000000;
*pData =60;
*pData =70;

## Slide 14
Case 4: constant pointer and constant data
uint8_t const * const pData = (uint8_t *)0x40000000;
Read-only pointer pointing to read-only data
Use case:
uint32_t read_status_register(uint32_t const * const pStatusReg){…}
Read from register’s value(it’s value 不應該被修改)
=> if 修改register status => lead to crash!

## Slide 15: Usage of ‘const’ and ‘volatile’ together
Example:
uint8_t volatile *const pReg = (uint8_t *)0x40000000;
const => 防止pointer被意外修改
Volatile => 在位址0x40000000的資料可能時常修改,不要優化此pointer上的任何讀寫操作

## Slide 16
uint8_t const volatile *const pReg = (uint8_t *)0x40000000;
此位址(0x40000000)上的data是易改變的, 但告訴programmer此位址上的data是不能改變的

## Slide 17: Case of reading from read-only buffer or address which is prone to unexpected change
uint8_t const volatile *const pReg = (uint8_t *)0x40000000;
Input data register of a peripheral
Or a shared memory from which you are supposed to read-only
Data coming frm external world
0xF1
Programmer 不應該修改此位址上的data
但此位址上的data可能會被外部世界的data所改變的
此位址仍然可以進行意外修改，但programer不應該做